## Slide 1: Single Image Haze Removal Using Dark Channel Prior
Paper author：Kaiming He
Jian Sunxx
Xiaoou Tang

## Slide 2
怎么得来的？
  由 推得
求A
怎么求？
估算
提出暗原色先验
优化
Soft matting 方法
暗原色先验去雾流程图

## Slide 3: content
The Standard Image Formation Model
Dark Channel Prior
Estimating the Transmission
Optimize Transmission Using Soft Matting
Estimating the Atmospheric Light
Recovering the Scene Radiance
Patch Size
Drawbacks

## Slide 4: The Standard Image Formation Model
Image degradation model
  The degradation processing of image can be modeled as a degradation function and a additive noise term：
  where is non-degraded value, is degraded value, is additive noise, is system function.
+

## Slide 5
Attenuation of light in atmosphere:
The radiant intensity of the unit volume in the direction of the observer is:
is wavelength of the light，
is the angle as shown in the picture,
scattering coefficient，
is radiant intensity of incident light.
Quoted from Shree K. Nayar and Srinivasa G. Narasimhan “Vision in Bad Weather”

## Slide 6
The intensity scattered by the lamina is :
The total flux(in all directions)scattered by this lamina is:
is the total scattering coefficient.
Then
By integrating the limits x = 0 and x = d , we get:
is transmission, and is written as t(x) in the paper

## Slide 7
Airlight
Caused by the scattering of environmental illumination by particles.
Increases with pathlength.
Irrespective type of environmental illumination incident upon dV , its intensity is:
is the total scattering coefficient, k is proportionality constant
Reason
Characteristic
Quoted from Shree K. Nayar and Srinivasa G. Narasimhan “Vision in Bad Weather”

## Slide 8
View element dV as a source with intensity ,
the irradiance it produces is:
the radiance of dV is:

## Slide 9
Then we get:
Integrating this expression:
Setting to get Rewrite the expression:
is the atmospheric light A in the paper

## Slide 10
Hazy image model
The spectral distribution received by the observer is a sum of the distributions of directly transmitted light and airlight.
is the observed intensity, is the scene radiance, A is the atmospheric light, is medium transmission.
Picture quoted from Yoav Y. Schechner, Srinivasa G. Narasimhan, and Shree K. Nayar “Polarization-based vision through haze”

## Slide 11: Dark channel pror
Based on observation:
In most of the nonsky patches, at least one color channel has some pixels whose intensity are close to zero.
is a color channel of J and is a local patch centered at .
Reasons for its existence:
a) shadows
b) colorful objects or surfaces
c) dark objects or surfaces

## Slide 12
Verify its correctness:
Select 5,000 images and manually cut out the sky regions. Their dark channels are computed using a patch size 15×15.
Statistical result:
Image size: 500x500, patch size: 15x15
75% dark channel values = 0
86% dark channel values < 16
90% dark channel values < 25
Notes: The dark channel prior is not a good prior for the sky regions.

## Slide 13
Original image
Min(R,G,B)
Dark channel

## Slide 14
Original image
Min(R,G,B)
Dark channel

## Slide 15: Estimating the Transmission
Normalize the haze imaging equation：
Assume that the atmospheric light A is given，then
Calculate the dark channel:
In fact
Assume that the transmission in a local patch is constant, denote transmission as , put the minimum operators on both sides.
Use the minimum filter, its complexity is linear to the image size

## Slide 16
Notice is a haze-free image, the dark channel of J is close to zero:
This leads to:
We can eliminate the multiplicative term and estimate the transmission simply by

## Slide 17
Sky regions :
The dark channel prior is not a good prior for the sky regions. But the color of the sky in a hazy image is usually very similar to the atmospheric light A. So, in the sky region have
Then

## Slide 18
Correction parameter :
Even on clear days the atmosphere is not absolutely free of any particle.
The presence of haze is a fundamental cue for human to perceive depth. It is called aerial perspective.
Remove the haze thoroughly, the image may seem unnatural and we may lose the feeling of depth.
So, introduce a constant parameter to keep a small amount of haze:
Here,
Reason

## Slide 19
Original image

## Slide 20: Soft matting: optimize
Image matting equation:
where and are foreground and background colors, is the foreground opacity.
Compare with

## Slide 21
The author derive a cost function from local smoothness assumptions on foreground and background colors.
  Solve a sparse linear system of equations to find the globally optimal
A closed-form framework of matting
A.Levin, D. Lischinski, and Y. Weiss “A Closed Form Solution to Natural Image Matting”
Source
Abstract
where is some large number, is a diagonal matrix whose diagonal elements are one for constrained pixels and zero for all other pixels, and is the vector containing the specified alpha values for the constrained pixels and zero for all other pixels.
quoted from
Quoted from A.Levin, D. Lischinski, and Y. Weiss “A Closed Form Solution to Natural Image Matting”

## Slide 22
Denote the refined transmission map by . Rewriting and in their vector forms as t and ,
where the matrix L is called the matting Laplacian matrix. Its (i , j) element is defined as
Apply it to refine the transmission.
where and are the colors of the input image I at pixels i and j,
is the Kronecker delta, and are the mean and covariance matrix of the colors in window , is a 3×3 identity matrix, is a regularizing parameter, is the number of pixels in the window .

## Slide 23
L is based on a color line assumption: The foreground / background colors in a small local patch lie on a single line in the RGB color space.
Derivation of L
The color line assumption is valid in the problem of haze removal for the following reason：
First, the scene radiance J is a natural image, the color line model holds for natural images.
Second, the atmospheric light A is a constant, which satisfies the assumption.

## Slide 24
The optimal t can be obtained by solving the following sparse linear system:
U is an identity matrix of the same size as L, is a constant parameter ( in the experiments).
This framework is mainly used to extrapolate the values into the unknown regions.
Notes

## Slide 25
Bilateral filter:
After solving the linear system, then perform a bilateral filter on t to smooth its small scale textures.
The refined results show that the halos and block artifacts are suppressed.

## Slide 27: Estimating the Atmospheric Light
Previous Work:
The brightest pixels in the hazy image are considered to be the most haze-opaque.
Ignore sunlight, scene radiance of each color channel is given by
where is the reflectance of the scene points.
Rewrite the haze imaging equation as:
Tan’s work , “Visibility in Bad Weather from a Single Image”
𝐼(𝑥)=𝐽(𝑥)𝑡(𝑥)+𝐴[1−𝑡(𝑥)]

## Slide 28
In practice we can rarely ignore the sunlight. Considering the sunlight S, then
Drawback
×
×

## Slide 29
Use the dark channel to detect the most haze-opaque region
Pick the top 0.1 percent brightest pixels in the dark channel.
Among these pixels, the pixels with highest intensity are selected as the atmospheric light.
This method works well even when pixels at infinite distance do not exist in the image.
is top 0.1 percent brightest pixels in the dark channel.
Notes

## Slide 30
(a) Input image. (b) Dark channel and the most haze-opaque region. (c) The patch where is choose as atmospheric light. (d),(e) Two patches that contain pixels brighter than the atmospheric light.
(a)
(b)
Quoted from “Single Image Haze Removal
Using Dark Channel Prior”

## Slide 31
When pixels at infinite distance do not exist in the image
(a) Input image. (b) Dark channel. The red pixels are the most haze-opaque regions detected the method. (c) Haze removal result.
(a)
(b)
(c)
Quoted from “Single Image Haze Removal
Using Dark Channel Prior”

## Slide 32: Recovering the Scene Radiance
Restrict the transmission
Set a lower bound . With the atmospheric light A and the transmission map , recovered by
Increase the exposure
The image after haze removal looks dim, so increase the exposure of for display.
𝐼(𝑥)=𝐽(𝑥)𝑡(𝑥)+𝐴[1−𝑡(𝑥)]

## Slide 33
Input image
Input image
Haze removal result
Haze removal result

## Slide 34: Patch Size
patch size
The probability that a patch contains a dark pixel is increased.
The assumption that the transmission is constant in a patch becomes less appropriate

## Slide 35
A haze-free image and its dark channels (b)using 3x3 and (c)using 15x15 patches
Hazy image and the recovered scene radiance using (b) 3x3 and (c)15x15 patches. The recovered scene radiance is oversaturated for a small patch size, while it contains apparent halos for a large patch size.
(b)
(c)
(b)
(c)
(a)
(a)
Quoted from “Single Image Haze Removal
Using Dark Channel Prior”

## Slide 36
(a) Input hazy images. (b) Using 3x3 patches. (c) Using 15x15 patches. (d) Using 30x30 patches
(a)
(b)
(c)
(d)
Quoted from “Single Image Haze Removal
Using Dark Channel Prior”

## Slide 37: Drawbacks
When haze imaging model is physically invalid
When scene objects are inherently similar to the atmospheric light.
Constant-airlight assumption may be unsuitable when the sunlight is very influential.
The transmission t is wavelength dependent if the particles in the atmosphere are small.

## Slide 38
Thank you!

## Slide 39
流程图
目录
退化函数
成像模型
光的散射衰减
暗原色先验
环境光的干扰
成像模型
估算透射率
优化透射率
估算大气光
观察发现
产生原因
验证
天空区域
应用先验
计算暗通道
调节参数
用于优化透射率
封闭式结构抠图
抠图方程
忽略太阳光
用暗通道
复原图像
设置阈值
增强曝光
分块尺寸的影响
存在的缺陷
PPT结构图

## Slide 40
  感谢何恺明、孙剑、汤晓鸥三位大师的这篇论文，让我从中学到了不少东西，另外非常感谢我的老师郑海永的悉心指导。 PPT的大部分内容用的也是这篇论文的原文，少部分引用了其他几篇论文，其中一部分雾图是从网上下载的。